Electric Current Charge and Power:

Your specification says:

An electrical current is a flow of tiny charged particles called e________.

When electrons pass through components like r___________s or lamps they are prevented from moving as easily

Try to match the power rating with the device:

# Text boxes

•  Electric current is the rate of flow of charge.

•  When an electrical charge flows through a resistor, electrical energy

is transformed into heat energy.

•  The rate at which energy is transformed in a device is called the

power.

e_________

c_________

Flowing e________ hindered by particles in the r_________

Resistor

E_____y is lost by the e________ and is given off as h________

The power of a device

All electrical devices transfer e______. The rate at which they transfer energy is called the p_____ of the device.

Power is measured in w______.

The devices which use most power are those which produce lots of heat.

Devices which produce s_______  are generally low p________.

Washing machine

Kettle

CD player

T.V.

Electric Shower

Calculator

3 000W

2000W

20W

350W

7000W

0.0009W

A kettle transforms 2000 Joules of electrical energy into heat energy every second.

An electric shower transforms 7 000 j______ of electrical energy into h____ energy every second

A T.V transforms 350J of electrical ______ into light e________ and s________ energy every second.

The power formula:  allows us to work out the current flowing through any device.

power (W) = current(A) x potential difference(V)

The mains voltage in this country is 230V

And the current flowing through a mains appliance is

The power of the appliance

230V

This is how we work out the size of f____ that an appliance needs.

For example:		a 2300W kettle

2300W

230V

=10A

Choosing between a 13A, 10A %A and 3A fuse we choose the 13A fuse for the kettle as all of the others would blow,.