# MAINS ELECTRICITY WORTHROUGH

Your specification says you have to be able to:

| Wire | Colour |
| --- | --- |
| Live |  |
| Neutral |  |
| Earth |  |
| Safety device | How it works |
|  | Melts when too much current flows |
|  | Protects from shock with metal cased appliances |
|  | Grips outer cable and prevents strain on the inner coloured wires |

## 3 Core cable

## MAINS ELECTICITY COMPARED WITH ELECTRICITY FROM BATTERIES

Your specification says you have to know that:

Cells and batteries provide direct current (d.c)

Mark on the diagram the way the electrons flow around the circuit. This is called d_______  c_________.

The mains supplies an electric current which is constantly c________g  d_________n

this is called a_____________ c___________. The two letter abreviation for this is  ____

In the UK the mains current changes dirrection  ______  times every second.

We say that the mains is an a.c. supply with a frequency of  ____ H_____ (Hz).

We show an a.c. supply like this on a diagram:

The voltage supplied by the mains is ______V.

## Graphs and oscilloscopes

Your specification says you must:

An oscilloscope traces a graph of v_______ against t______ on a screen.

# Text boxes

Know that most electrical appliances are connected to the mains using cable and a three-pin plug.

Know how to wire a three-pin plug

Recognise errors in the wiring of a three-pin plug

Recognise dangerous practice in the use of mains electricity

Label the diagram:

neutral wire 	 live wire	earth wire 	cable grip

outer cable	fuse

The job of the fuse

A fuse prevents too much electric ________ flowing.  If too much current flows wiring gets very hot and may give off poisonous _______ or even burst into ______

Lables:  Inner conducting wires made of copper

coloured insulating sleeving wire        live 		neutral 	earth

outer PVC insulating cable

Cells and batteries supply current which always passes in the same

direction. This is called direct current (d.c.).

An alternating current (a.c.) is one which is constantly changing

direction. Mains electricity is an a.c. supply. In the UK it has a

frequency of 50 cycles per second (50 hertz).

UK mains supply is about 230 volts.

know how to compare potential differences of d.c. supplies and the peak

potential differences of a.c. supplies from diagrams of oscilloscope

traces

Draw on the diagrams

1. the trace for a positive d.c. potential difference

2. the trace for a negative d.c. potential difference

3. the trace for an alternating potential difference

3. the trace for an alterm