# FUSES, CIRCUIT BREAKERS AND EARTHING

Your specification says:

Fuses are there to prevent _______ and electrical shocks from faulty appliances.

A fuse is a piece of wire with a low m_______  p_________. Sometimes it is enclosed in a glass tube with metal ends:

The fuse is designed to melt (b_____) when a current of a particular value flows through it.

The fuse here is designed to blow when ____  amps of electric current is flowing.

In 3 pin plugs the common fuses which are used are:

____A,    _____A    ______A   _______A

Appliances sometimes have internal _______ which give further protection.

If a table lamp has two amps of electric current flowing through it in normal operation. The plug should be fitted with a ____A fuse. If the lamp becomes faulty and too much c______ flows the fuse will ______ when ___A flows.

## Circuit Breakers

Modern houses are fitted with circuit _________ rather than f______.

Circuit breakers have several advantages:

- A fuse takes a good fraction of a s_______ to blow wheras if a fault develops a circuit breaker switches off much more quickly. This can save l_____.

- Circuit breakers can be re____ when the fault is fixed.

- No special skills are needed to reset a circuit breaker. Mending a mains fuse can be dangerous if you do not know what you are doing.

## Earthing

The y________ and g_______ wire in the plug does not normally carry any e______ c_______. It is a safety device.

If there is a fault and the Earth is not connected to the cooker

# Text boxes

- If an electrical fault causes too great a current the circuit should be

switched off by a fuse or a circuit breaker.

- When the current in a fuse wire exceeds the rating of the fuse it will

melt, breaking the circuit.

- Appliances with metal cases are usually earthed.

- The earth wire and fuse together protect the appliance and the user.

A kettle normally takes 10A. It should not be fitted with a 10A ______ because the fuse would  _______. A better fuse to use would be a ___A fuse.

The Earth Socket is connected to a large m_____ plate buried in the g______  So when you plug in an appliance. The green and yellow lead just leads to the gr_______

The Earth Lead in an appliance is connected to its m______ case.

live wire frays and touches the case

The current finds the easiest route to _____ through Sally Chef!

If there is a fault and the earth is connected to the case

Frayed live wire touches the m______ c_____.

The current again takes the easiest route to E____ but this time it is safely through the e______ connection

Large c_____ runs to Earth and fuse b______