1.	A 1.0 µF capacitor is charged by means of a constant current of 10 µA for 20s.  What is the energy finally stored in the capacitor?

A 4.0 × 10-4J

B 2.0 × 10-3J

C 2.0 × 10-2J

D 4.0 × 10-2J

3

4

7 A 1000 µF capacitor, initially uncharged, is charged by a steady current of 50 µA.  How long

will it take for the potential difference across the capacitor to reach 2.5V?

A 20 s

B 50 s

C 100 s

D 400 s

8 In experiments to pass a very high current through a gas, a bank of capacitors of total

capacitance 50 µF is charged to 30 kV.  If the bank of capacitors could be discharged

completely in 5.0ms what would be the mean power delivered?

A 22 kW

B 110 kW

C 4.5MW

D 9.0MW

# Text boxes

2