# Notes on error (uncertainty)

Remember on a single measurement of length the estimated uncertainty is as follows

| instrument | Estimated uncertainty |
| --- | --- |
| rule | 1mm |
| vernier | 0.1mm |
| micrometer | 0.01mm |

1. A single reading on a rule of 20.1 cm becomes 20.1± 0.1 cm when the uncertainty is taken into account’

If you take several readings of length the uncertainty is half the spread of results

e.g. measuring a length of wire by four students gave these results:

Measurement of length of wire (cm)

10.2

10.4

10.6

10.5

So we  can write

2. mean value± the uncertainty	   in this case  			10.4 ± 0. 2cm

----------------------

# Percentage uncertainty

The percentage uncertainty is simply 				estimated uncertainty___________ x 100

measured value  (the mean value in the second case)

So in 1 above    the percentage uncertainty is  ( 0.1/20.1) = 0.5%

The value can be written as 20.1±0.5%

In 2 above the percentage uncertainty is           (0.2/10.4) = 2.0%

The value is written as			 10.4 ± 2.0%  cm

When multiplying or dividing quantities the percentage uncertainties are added

So if we multiply 1 by 2

20.1 x 10.4 = 209.04  ie 209.0 to 1 decimal place

Adding the percentage uncertainty:   0.5 + 2.0 = 2.5%

So the final figure is written as              209.0   ±   2.5%   cm

# Text boxes

The spread of results is   10.6 -10.2 cm = 0.4cm

The uncertainty is half the spread = 0.2cm