# Experiment: Finding the Position of a Virtual Image:

### 1. The plane mirror:

The image visible in a plane mirror appears behind the mirror. it is a virtual image.

You will find its distance by parallax.

- Place a fixed pin in front of the plane mirror. Place a second pin behind the mirror so that the top of the pin can be seen superimposed over the reflection when the eye is in line.

- Keep only one eye open and move the eye from side to side.

- Generally the reflection in the mirror will appear to move out of line with the pin behind the mirror.

- Place the pin at different distances until the image in the mirror and the pin behind the mirror always coincide when the eye is moved.

- Measure the distance of the object pin and the pin behind the mirror which is now at the distance of the virtual image within the mirror.

### 2 The Converging Lens.

The process is similar to the plane mirror though more difficult to do accurately. .The object pin must be placed a distance from the lens which is less than its focal length.

Look through the lens.

The virtual image of the pin can be seen.

- Using the parallax principle move the eye from side to side .

- Move the clamp and pin until the pin can be seen superimposed above the virtual image.

- The angle is limited as the edge of the lens tends to distort the image.

- Measure the distance from the lens axi to the object and to the virtual image.

- Calculate the focal length of the lens using the lens formula.

# Text boxes

object pin

clamped moveable optical pin

lens

pin board

pin board

mirror

moveable optical pin

fixed optical pin

virtual image of the pin