# Definitions

| stress | Force per unit of cross sectional area F/A (N/m2 = Pa { pascals}) |
| --- | --- |
| strain | Change in length / original length ΔL/L (no unit) |
| Hooke’s Law | Up to some maximum load (the limit of proportionality) the extension of a spring or wire is proportional to the applied load. |
| the limit of proportionality | The maximum point at which the extension of the wire or spring increases in direct proportion to the load applied. |
| Elasticity | A material is said to be elastic if it returns to its original size or shape when the load which has been deforming it is removed. |
| Elastic Limit | The maximum load which a body can experience and still return to its original size and shape one the load is removed. (This does not always coincide with the limit of proportionality) |
| Yield Point | Under a load there is a point beyond the elastic limit where a large increase in extension begins and a reduced force will continue to extend the body. This is due to a change in internal structure. |
| Strength | The strength of a material refers to the maximum force which can be applied to a material without it breaking. |
| Breaking stress | The maximum stress that the material can withstand. (the ultimate tensile strength) |