| QUESTIONS ON HOOKE’S LAW |  |
| --- | --- |

1.	A spring is 20 cm long when a load of 10 N is hanging from it, and 30 cm long when a load of 20 N is

hanging from it. Draw a graph to work out the length of the spring when:

a]	there is no load on it;

b]	there is a load of 5 N on it.

(Plot x = load, y = spring length )

2.	In a spring experiment, the results were:

| load (N) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| length (mm) | 50 | 58 | 70 | 74 | 82 | 90 | 102 | 125 |
| extension (mm) |  |  |  |  |  |  |  |  |

a]	What is the length of the spring when unstretched?

b]	Copy and complete the table.

c]	Plot a graph of the data.  (Plot x = load, y = spring extension)

d]	One of the results is wrong.

(i) Which?		(ii) What should the result be?

e]	Mark the elastic limit on your graph.

f]	What load would give an extension of 30 mm?

g]	What would be the spring length for a load of 4.5 N?

3. 	An engineer needs to know how far a long beam will sag under a load. The table shows some results:

| load (N) | 1000 | 2000 | 3200 | 4400 | 5200 | 6500 |
| --- | --- | --- | --- | --- | --- | --- |
| sag (cm) | 2.0 | 4.0 | 6.6 | 8.8 | 10.4 | 13.4 |

a]	Plot a graph of the sag against load. (Plot x = load, y = sag)

b]	One of the measurements for sag is wrong.

(i) Which?			(ii) What should the result be?

c]	What would be the sag for a load of 4500 N?

d]	What load would give a sag of 5.2 cm?

e]	Would a longer beam sag more or less? Sketch its graph on the same axes.

4.	Some students carry out an experiment to find out how a spring stretched when loads were added to it.

a]	Draw a labelled diagram to show what is meant by the extension of the spring.

The results of the experiment are shown in the table. One of the readings is incorrect.

| load (N) | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| extension (mm) | 0 | 16 | 32 | 58 | 64 | 80 | 96 | 112 |

b]	Use these results to plot a graph.  (Plot x = load, y = spring extension)

c]	Use your graph to find	(i) the extension when the load is 3 N;

(ii) the load which produces and extension of 40 mm.

d]	Label the incorrect point on the graph with the letter E.

5.	A light spring obeying Hooke’s law was attached to a fixed support. When a 5 N load was hung on it,

the length of the spring was 160 mm. When a 10 N load was hung on it, the length became 200 mm.

Find:		a]	the length of the spring with no load;

b]	the length of the spring with a load of 8 N.